## Slide 1: Python Networking 101
© 2017 Presidio, Inc. All rights reserved. Proprietary and Confidential. Use of any part of this document without the express written consent of Presidio, Inc. is prohibited.

## Slide 2
Lesson Plan
Walk through the goal of the class.
Teach overview of what Python is and what it can do.
Run Interpreter and do a “Hello World”.
Write “Hello World” as a script and run it.
Complete task One.
Discuss Includes and Libraries.
Introduce Netmiko and the Connection class.
Write first connection class to attach to switch.
Design commands to read port status and return NUC ports.
Complete Task Two.
Learn to go into Enable mode.
Learn basic error handling.
Learn to send commands!
Complete Task Three.

## Slide 3
Goals
Getting over the “where do I start” question
The goal of the class is to have each engineer complete the following tasks:
1. Establish connectivity to the switch, logon, logoff, and delete the connection.
2. Logon, and determine which ports have devices attached to them.
3. Create a VLAN sub-interface on each of the 3 ports and set the Description of the interface to their name.
“There is a myth that writing code is hard, that it something meant for others, but not you. While it can be hard and take years to master, the goal should be to learn enough to help you with your job and be happy with that.”

## Slide 4
Python
Interpreted, not Compiled
Easy to Read
#2 behind Javascript
myint = 42 is literally (0101010 bin)
mystring = “42” is literally (0x34 0x32 UTF-8)
Remember 42 != “42”
Build strings: mynewstring = “This is the answer to the universe: “ + mystring
# Note: remember the space at the end of the string to insert a space!

## Slide 5
Objects
Think of a model of a gokart. Build all the parts you need in code. Then others can import your code.
Kart Class:
horsepower = 45
turnangle = -20
tires = 0.9
gas()
brake()
turn()
Then to use it, just call Kart.gas(0.5) or Kart.turn(-20)

## Slide 6
Problem - Instance
Need 2 Karts to race!
How to fix = Instance
Create an instance calling the constructor Kart(hp, turnangle, tirewear)
kartone = Kart(50, 0, 1)
karttwo = Kart( 40, , .8) note: middle value is default
Then use: kartone.turn(20)
karttwo.brake(-2)

## Slide 7
Other functions
Python has built in functions for many data types.
For example, when you define a string variable, you can have many built in actions for that string:
mystring = “This is my string!”
myuppercasestring = mystring.upper()
myuppercasestring is now = “THIS IS MY STRING!”
Can ‘split’ strings mystring.split() = [“This”, “is”, “my”, “string!”]

## Slide 8
Lab # 1- Running Code
Run Hello World in Interpreter
>>> print(“Hello Network!”)
Run Hello World as a Script
print(“Hello Network!”)
From location you saved the file: python hellonetwork.py
or: python3 hellonetwork.py

## Slide 9
Includes
Pre-built code library you can “include” in your code.
Netmiko is a pre-built ssh and network code library
from netmiko import ConnectHandler
Adds lots of functions you can use to program your equipment

## Slide 10
Netmiko
net_connect.config_mode() -- Enter into config mode
net_connect.check_config_mode() -- Check if you are in config mode, return a boolean
net_connect.exit_config_mode() -- Exit config mode
net_connect.clear_buffer() -- Clear the output buffer on the remote device
net_connect.enable() -- Enter enable mode
net_connect.exit_enable_mode() -- Exit enable mode
net_connect.find_prompt() -- Return the current router prompt
net_connect.commit(arguments) -- Execute a commit action on Juniper and IOS-XR
net_connect.disconnect() -- Close the SSH connection
net_connect.send_command(arguments) -- Send command down the SSH channel, return output back
net_connect.send_config_set(arguments) -- Send a set of configuration commands to remote device
net_connect.send_config_from_file(arguments) -- Send a set of configuration commands loaded from a file

## Slide 11
Connect to Switch - Steps
# Connect to the Switch
# Get the prompt output to a variable
# Print the Prompt output
# Disconnect from the Switch
# Exit

## Slide 12
Connect to Switch – Required information
Switch IP Address: 192.168.128.151
Switch Type: IOSXE
SSH Login Name: admin
SSH Password: cisco123!
Enable Password: Cisco123!
Netmiko uses SSH to make a connection and pass very familiar IOS commands to the switch, and performs output parsing for you.
Netmiko can also make configuration changes.

## Slide 13
Connect to Switch - Code
from netmiko import ConnectHandler
# set un equal to your username
# set pw equal to your password
un = "admin"
pw = "cisco123!”
ios_type = “cisco_xe”
ip_addr = “192.168.128.151”
net_connect = ConnectHandler(device_type=ios_type, ip=ip_addr, username=un, password=pw)
output = net_connect.find_prompt()
# 'LAB'>’ – Returns the current prompt as Unicode string
print(output)
net_connect.disconnect()
exit()

## Slide 14
Getting Switch Information - Steps
# Connect to the Switch
# Send a Command to get list of Active Interfaces
# Print the Command output
# Disconnect from the Switch
# Exit

## Slide 15
Getting Switch Information - Code
from netmiko import ConnectHandler
# set un equal to your username
# set pw equal to your password
un = "admin"
pw = "cisco123!"
ios_type = “cisco_xe”
ip_addr = “192.168.128.151”
net_connect = ConnectHandler(device_type=ios_type, ip=ip_addr, username=un, password=pw)
output = net_connect.send_command('show ip int brief | include up')
print(output)
net_connect.disconnect()
exit()
Output:
Vlan1 192.168.128.151 YES NVRAM up up
GigabitEthernet0/7 unassigned YES unset up up
GigabitEthernet0/8 unassigned YES unset up up
GigabitEthernet0/9 unassigned YES unset up up

## Slide 16
But what if we wanted to know each interface description?
from netmiko import ConnectHandler
# set un equal to your username
# set pw equal to your password
un = "admin"
pw = "cisco123!"
ios_type = “cisco_xe”
ip_addr = “192.168.128.151”
net_connect = ConnectHandler(device_type=ios_type, ip=ip_addr, username=un, password=pw)
output = net_connect.send_command('show int description | include up')
print(output)
net_connect.disconnect()
exit()
Output:
Vl1 up up
Gi0/7 up up Meraki MX67 WAN port
Gi0/8 up up raspberry pi 1
Gi0/9 up up Cisco 3560CX

## Slide 17
What about finding the connected neighbors via CDP?
from netmiko import ConnectHandler
# set un equal to your username
# set pw equal to your password
un = "admin"
pw = "cisco123!"
ios_type = “cisco_xe”
ip_addr = “192.168.128.151”
net_connect = ConnectHandler(device_type=ios_type, ip=ip_addr, username=un, password=pw)
output = net_connect.send_command('show cdp neighbors')
print(output)
net_connect.disconnect()
exit()
Output:
Device ID Local Intrfce Holdtme Capability Platform Port ID
3560CX.kupjones.com
Gig 0/9 137 S I WS-C3560C Gig 0/7
Total cdp entries displayed : 1

## Slide 18
Lab 2 – Log on and Enable - Steps
Connect to the Switch
Get the prompt output to a variable
Print the Prompt output
Enter “Enable” Mode
Get the prompt output to a variable & Print the Prompt output
Disconnect from the Switch & Exit
The difference is we are using the Netmiko library to parse output data for us instead of passing IOS commands

## Slide 19
Lab 2 – Log on and Enable - Code
from netmiko import ConnectHandler
un = "admin"
pw = "cisco123!"
se = "Cisco123!"
ios_type = "cisco_xe"
ip_addr = "192.168.128.151"
net_connect = ConnectHandler(device_type=ios_type, ip=ip_addr, username=un, password=pw, secret=se)
output = net_connect.find_prompt() # 'LAB'>’ – Returns the current prompt as Unicode string - note prompt
print(output)
net_connect.enable()
output = net_connect.find_prompt() # 'LAB'#’ – Returns the current prompt as Unicode string - note enable prompt
print(output)
net_connect.disconnect()
exit()

## Slide 20
Error Checking - Steps
Connect to the Switch
Enter “Enable” Mode
Get the prompt output to a variable & Check to make sure we are in “Enable” mode
Print Error if not in “Enable” mode
Disconnect from the Switch & Exit

## Slide 21
Error Checking - Code
from netmiko import ConnectHandler
un = "admin"
pw = "cisco123!"
se = "Cisco123!"
ios_type = "cisco_xe"
ip_addr = "192.168.128.151"
net_connect = ConnectHandler(device_type=ios_type, ip=ip_addr, username=un, password=pw, secret=se)
net_connect.enable()
checkerror = net_connect.find_prompt()
if not '#' in checkerror:
print("Error - Not in Enable Mode!")
else:
print("You are in Enable Mode")
net_connect.disconnect()
exit()

## Slide 22
Getting Interfaces – Steps
This time we are going to put the found interfaces into a data structure that we can use, instead of just outputting the interfaces to the screen (recall from our python intro – Lists).
Connect to the Switch & Enter “Enable” Mode
Get list of Active Interfaces
Convert String of Interface Output to List of Interface Names
              Split() Output String to a list of words
              Check if word has “Gi” (for GigabitEthernet) in the word
              If yes, add it to our List of Interface Names
Disconnect from the Switch & Exit

## Slide 23
Getting Interfaces - Code
from netmiko import ConnectHandler
un = "admin"
pw = "cisco123!"
se = "Cisco123!"
ios_type = "cisco_xe"
ip_addr = "192.168.128.151"
# Define a blank list of interfaces
interfacelist=[ ] ######################### NEW ############################
# connect to switch
net_connect = ConnectHandler(device_type=ios_type, ip=ip_addr, username=un, password=pw, secret=se)
net_connect.enable()
cmdoutput = net_connect.send_command('show ip int brief | include up')
outputlist = cmdoutput.split() ######################### NEW ############################
for eachword in outputlist:
if 'Gi' in eachword:
interfacelist.append(eachword)
print("Output of interfacelist list:")
print(interfacelist)
net_connect.disconnect()
exit()

## Slide 24
Getting Interfaces – Output Compared
Let us see what the “split” function actually does:
cmdoutput = net_connect.send_command('show ip int brief | include up')
cmdoutput string:
Vlan1 192.168.128.151 YES NVRAM up up
GigabitEthernet0/7 unassigned YES unset up up
GigabitEthernet0/8 unassigned YES unset up up
GigabitEthernet0/9 unassigned YES unset up up
outputlist = cmdoutput.split()
outputlist list:
['Vlan1', '192.168.128.151', 'YES', 'NVRAM', 'up', 'up', 'GigabitEthernet0/7', 'unassigned', 'YES', 'unset', 'up', 'up', 'GigabitEthernet0/8', 'unassigned', 'YES', 'unset', 'up', 'up', 'GigabitEthernet0/9', 'unassigned', 'YES', 'unset', 'up', 'up']
for eachword in outputlist:
if 'Gi' in eachword:
interfacelist.append(eachword)
interfacelist list:
['GigabitEthernet0/7', 'GigabitEthernet0/8', 'GigabitEthernet0/9']

## Slide 25
Lab 3 – Putting it all Together - Steps
Connect to the Switch & Enter “Enable” Mode – check for Error
Get list of Active Interfaces & Convert String of Interface Output to List of Interface Names
Build a List of Commands to set your VLAN & Send the Commands to the Switch
Build a List of Commands to set your VLAN to active ports trunks
  Iterate through list of Interface Names and Apply VLAN to each Active Interface
Disconnect from the Switch & Exit

## Slide 26
from netmiko import ConnectHandler
un = "admin"
pw = "cisco123!"
se = "Cisco123!"
ios_type = "cisco_xe"
ip_addr = "192.168.128.151”
interfacelist=[ ]
new_vlan = “20” ######################### NEW ############################
net_connect = ConnectHandler(device_type=ios_type, ip=ip_addr, username=un, password=pw, secret=se)
net_connect.enable()
checkerror = net_connect.find_prompt()
if not '#' in checkerror:
print("Error - Not in Enable Mode!")
else:
print("You are in Enable Mode")
Lab 3 – Putting it all Together – Code 1/4

## Slide 27
Lab 3 – Putting it all Together – Code 2/4
# Get list of interfaces, split, pull interface names into interfacelist list
cmdoutput = net_connect.send_command('show ip int brief | include up’)
outputlist = cmdoutput.split()
for eachword in outputlist:
if 'Gi' in eachword:
interfacelist.append(eachword)
print("Output of interfacelist list:")
print(interfacelist)

## Slide 28
Lab 3 – Putting it all Together – Code 3/4
# Build and send commands to build and name your VLAN
command1 = "vlan " + new_vlan #################### Space after ‘vlan’ is important!
command2 = "name " + un #################### Space after ‘name’ is important!
cmd_list = [command1, command2] #################### a list of commands is required
checkerror = net_connect.send_config_set(cmd_list) #################### the send_config takes the list as an argument
net_connect.exit_config_mode()
if not 'Invalid' in checkerror: #################### send_config sets an error code on exit for testing
print(command1 + " setup!") # Space before ‘setup’!
else:
print(“You failed to create the VLAN")
exit()
#VLAN Created!

## Slide 29
Lab 3 – Putting it all Together – Code 4/4
# Build and send commands to add your VLAN to active ports trunks
command2 = “switchport trunk allowed vlan " + myvlan # Space after 'add' important!
# Walk through interfacelist list and assign VLAN to trunk list
for interfacename in interfacelist:
command1 = "interface " + interfacename # Space after 'interface' important!
cmd_list = [command1, command2]
checkerror = net_connect.send_config_set(cmd_list)
#print(checkerror) # Want to see what IOS sees??? Uncomment this statement
net_connect.exit_config_mode()
if not 'Invalid' in checkerror:
print(command1 + " complete!")
else:
print("You failed to set the interface properly")
net_connect.disconnect()
print("Great job!!!")
exit()

## Slide 30
Goals
Getting over the “where do I start” question
Congratulations!
You have completed the following tasks:
  1. Established an ssh connection to a network device, logged on, and deleted the connection.
  2. Read data from a network device.
  3. Configure the network device programmatically.

## Slide 31
Goals
Getting over the “where do I start” question
From here – look at extending to using files for your config commands, using other libraries:
Add
Add multi-threading (pip install nornir) for logging into many devices at the same time
Try adding documenting to spreadsheets (pip install pandas) with the output of ciscoconfparse (pip install ciscoconfparse)
Use multiping (pip install multiping) for large ping lists
Check out advanced networking (pip install napalm)

## Slide 32: Additional Resources
DevNet
  Learn how to use Python to configure ACI, DNA Center, Meraki, and more
  https://developer.cisco.com/
Learnpython.org
  Free courses for Python
  https://www.learnpython.org/
PythonAnywhere
  Host, run, and code Python in the cloud
  https://www.pythonanywhere.com/
Learn Python 3 the Hard Way
  In-depth guide for learning Python
  https://www.amazon.com/Learn-Python-Hard-Way-Introduction/dp/0134692888
Automate the Boring Stuff
  How to do day to day tasks in python. Website free, can buy a book.
  https://automatetheboringstuff.com/

## Slide 33: THANK YOU